## Slide 1: Gas Transmission Access: Priority Rights
28 September 2017
First Gas / Presentation

## Slide 2
Agenda
What is Congestion
When could it occur
What the GTAC says about Congestion
What improvements could be made (in section 3 and/or elsewhere)

## Slide 3
Engagement with draft GTAC
Aug 2017
Dec 2017
Oct 2017
Telecon Q&A session (31 August)
Complete GTAC draft released for consultation and negotiation (10 August)
Stakeholder mark-ups and submissions on revised draft GTAC due (9 October)
Release of revised draft GTAC (11 September)
Sept 2017
Nov 2017
Submission of GTAC to GIC for review (8 December)
Ensure provisions of GTAC are well-understood before inviting mark-ups
Enable further revisions to be made to better achieve intent and eliminate ambiguities
Allow stakeholders to propose improvements and highlight any remaining concerns
Allow time for First Gas to review proposed changes and submissions
Allow stakeholders to review changes made following first round of mark-ups and obtain legal review/mark-ups
Allow time for First Gas to finalise the GTAC before submitting to GIC
Allow stakeholders further opportunity to address any unresolved issues (including issues raised by other parties prior to submission of final GTAC)
Initial run through session (17 August)
2-day workshop (24-25 August)
Workshop on revised draft GTAC (15 September)
Release of second revised draft GTAC (3 November)
Final mark-ups on second revised draft GTAC due (24 November)
Focused sessions on selected topics (21 & 28 September)
Jan 2018
Feb 2018
Mar 2018
* See GIC paper “Proposed approach to GTAC assessment” for further details on this stage
GIC complete review (by 23 March)
Submissions on GIC Preliminary Assessment due (23 February)
GIC releases Preliminary Assessment (22 December)

## Slide 4
What would Congestion look like?
Gas being gas, the most likely sign of actual Congestion would be a pressure problem, i.e. not enough of it
The problem would be quantified by reference to Security Standard criteria:
  Minimum acceptable pressures in pipelines
  Time to minimum acceptable pressure (@ current -dP/dt)
Congestion is unlikely to occur “instantly”: more likely a gradual deterioration
Congestion could appear as a local (Delivery Point) problem, e.g. regulator instability and possible relief valve feathering
  Serious, but much less likely than a pipeline issue
The Critical Contingency Regulations require physical demand curtailment

## Slide 5
Congestion: when could it occur?
Congestion can arise if:
  Aggregate NQs (= requests for DNC) > Available Operational Capacity
  Actual offtake > Available Operational Capacity
Available Operational Capacity is a function of pipeline and DP capacity
FG will try to predict Congestion:
  AMP, other modelling, monitoring, ICAs
  Require notification of significant new load
  Congestion may nevertheless occur during the year
More accurate NQs → more likely to see Congestion coming
FG will still use Interruptible Agreements
  They’re not a fully reliable alternative to PRs
FG looks for opportunities to invest, not live with the problem (if it occurs)

## Slide 6
Code Approaches
MPOC approach (the Ostrich?):
  The TSO curtails delivery NQs: ta da! problem solved
  The affected Interconnected Party must curtail, however it can
VTC approach (feudalism?):
  If you’ve got Reserved Capacity you’re OK
  If you can’t get any, you’re stuffed
GTAC approach (market rules, OK?):
  No more legacy rights to capacity: equal opportunity access
  Enable scarce capacity to be obtained by parties who value it the most
Priority Rights are a key part of the GTAC
  The PEA wanted it
FG will seek Interruptible Load (s10.5) as a Congestion management tool
  Could be enough on its own / might not get any

## Slide 7
Priority Rights under GTAC
Delivery Zones will exclude Congested Delivery Points (s.3.4)
  Congestion may occur during a year (s.3.16)
At a Congested DP / group of DPs, FG will offer PRs up to AOC (s.3.5, 3.7)
PRs allocated by auction only (s3.9). FG will notify (s3.10) ≥ 10 days before :
  The Delivery Point(s)
  Number of PRs
  PR Term (6 Months initially)
  Reserve Price ($/PR)
  No auction if congestion eases (s3.17): PRs may be cancelled
  Shippers may bid ($/PR) for PRs: up to 5 tranches, different prices
FG will allocate PRs in descending order of bid price (s3.11)
Shippers may trade PRs (s3.12, 3.13)

## Slide 8
Who gets Priority Rights?
Those who bid the most, get the most
Most Dedicated Delivery Points will be included in Delivery Zones
Up to ~13 Dedicated Delivery Points may not initially be in a Delivery Zone, because:
  For some while yet they’ll be supplied under a Supplementary Agreement
  We’re haven’t yet decided otherwise
Should the PR Auction terms say anything about “who, or why”?
  Ban hoarding (use them or lose them)?
All PR Charges will be credited to Shippers (s11.14), pro-rata on DNC Charges
  FG is financially indifferent

## Slide 9
Use of Priority Rights
PRs ≠ Reserved Capacity: a Shipper must still nominate for DNC (s3.15)
  Regardless, the PR Charge is payable (s3.14)
Changed Provisional NQs have precedence (s4.19). Then, on the Day:
  Approved Intra-Day NQ > later Intra-Day NQs?
  Or, should we make each Intra-Day cycle a fresh start?
Option 1: Align PRs precisely with NQs for DNC
  Shipper must nominate to use PRs
Option 2: PRs a standing right
  At every nominations cycle, including Intra-Day, a Shipper has priority up to the level of its PRs
  But still, Shipper must nominate to use PRs

## Slide 10
Views
Suggested improvements?
Got a better idea? Let’s hear it